This page was exported from Pana-Pacific [    https://www.panapacific.com    ]

Export date: Wed Apr 17 11:45:05 2024 / +0000 GMT

# APTIV MACK HEAVY-DUTY AM/FM/WB WITH FRONT PANEL USB PORT, INTEGRATED SIRIUSXM SATELLITE RADIO AND INTEGRATED BLUETOOTH® – PP107224

SKU: PP107224

## Product Summary

COMMON FEATURES FOR ALL HEAVY-DUTY APTIV RADIOS:

- HEAVY-DUTY DESIGN – made for a commercial vehicle driver by having larger buttons and a heavy-duty construction for tougher environments.

- SAE J1455 COMPLIANT – meets all the test standards for reliability of an electronic component in a commercial vehicle.

- WEATHER BAND (WB) – offers National Weather Radio Broadcasts from over 1,025 locations throughout the United States on seven VHF/FM frequencies free-of-charge to provide continuous weather information 24 hours a day. Range: 162.400 MHz – 162.550 MHz

- ISO CONNECTOR – allows the radio to be connected directly to the vehicle's harness; no additional harness is required – no cutting, no separate accessories to purchase for all commercial vehicles manufactured with the ISO connect harness.

- FRONT AUX INPUT (MUSIC PORT) – easy access to plug in a smart device and enjoy your digital music library through the vehicle's speakers.

- REAR AUX INPUT – provides an auxiliary terminal for permanent hard wire to the rear side of the radio.

- SAE J1939 COMPLIANT – allows the different vehicle components that run on the communication bus system to talk to each other, compatible with most digital steering wheel/rear-sleeper controls.

- QUARTZ ALARM CLOCK – convenient, built-in quartz alarm clock with one hour timer.

- OUTPUT POWER – 18 Watts x 4 Channels, 18 Watts x 2 Channels (24 Volt Radios)

- SOUND QUALITY (EQ) FUNCTION – select the sound type (Pop, Rock, Country, News, Jazz, Classical or Manual) to improve the dynamic range

- SEPARATE BASS, MID, TREBLE, BALANCE AND FADER CONTROL

- 6 AM / 12 FM RADIO PRESET BUTTONS

- AUTO STORE MEMORY

- AUTO BAUD RATE – capable of auto detecting the correct CAN bus baud rate to use at power up; the possible baud rate is 250K or 500K.

- MECHLESS – no Compact Disc (CD) Player

- SHALLOW CLASSIS – 86.5 mm in depth

- VF DOT MATRIX DISPLAY – three line display that maximizes the viewing area on the front of the radios. This allows for more information on the screen and minimizes the need to scroll.

- WHITE FAKRA AM/FM ANTENNA CONNECTOR – robust locking mechanism, small form factor with high speed capability which allows for better cable management.

- MOTOROLA TO FAKRA ADAPTER CABLE – AM/FM Radio Antenna Adapter Fakra Jack code B to Motorola DIN socket connector six-inch cable. Adapter cable included with each APTIV radio model until OEM truck manufacturers change wiring from Motorola to FAKRA.

PRODUCT FEATURES:

- Integrated SiriusXM Satellite Radio Tuner - offers 100+ channels of digital quality audio programming heard uninterrupted across the United States and Canada; a subscription is required to receive SAT broadcasts*

- SiriusXM 'Instant Replay' feature enabled - allows user to pause, rewind and replay audio content from the currently active channel

Built-in Bluetooth® profile is selectable between Audio Streaming and/or Hands-Free phone operation (utilizing the vehicle's audio system and a remote mic** - up to 10 devices can be easily stored in the radio

- memory for fast pairing)

- Front Panel USB Port – gives a direct connect location for memory devices with USB interface, to play stored music and/or charge the device and have iPod® control through the radio

- iPad® charging capability up to 2.1A

- Back-lit Display Lighting - BLUE

- Handheld Remote Control sold separately - Part No. PP603988

*Satellite Radio Antenna sold separately - Part No. PP802458 or SRTMM-02

*Bluetooth® Mic sold separately – Part No. PP603846 or PP604240

NOTE: THE APTIV MACK RADIOS PP107222, PP107223, AND PP107224, ARE FOR USE ONLY IN MACK TRUCKS AND ARE COMPATIBLE WITH MACK SOFTWARE.

A SPECIFIC ADAPTOR HARNESS MAY BE REQUIRED BASED ON TRUCK OPTIONS AS NOTED IN THE HARNESS GUIDE IN THE BACK OF THIS CATALOG. MACK TRUCKS BUILT AFTER 8/15/14 WILL NOT REQUIRE AN ADAPTOR HARNESS.

Product export as MS Document by WooCommerce PDF & Print plugin.